## Slide 2: WIFI MANAGER LIBRARY
Diễn giả: Nguyễn Hoàng Phúc
Bộ phận: IoT Indruino

## Slide 3: 1. WIFI CLASS
Đăng nhập vào một mạng wifi bằng cách cung cấp:
  Tên mạng
  Mật khẩu vào mạng
  Phương thức bảo mật
Cú pháp:
WiFi.begin(); WiFi.begin(ssid); WiFi.begin(ssid, pass); WiFi.begin(ssid, keyIndex, key);
Ví dụ:
#include <WiFi.h> //SSID of your network char ssid[] = "yourNetwork"; //password of your WPA Network char pass[] = "secretPassword"; void setup() { WiFi.begin(ssid, pass); } void loop () {}
1.1 WIFI.begin

## Slide 4: 1. WIFI CLASS
Đăng xuất khỏi mạng đang được kết nối trong thời điểm hiện tại
Cú pháp:
WiFi.disconnect();
1.2 WIFI.disconnect

## Slide 5: 1. WIFI CLASS
Cho phép bạn định cấu hình địa chỉ IP tĩnh cũng như thay đổi địa chỉ DNS, cổng và mạng con WiFi.
Gọi WiFi.config () trước khi WiFi.begin () để định cấu hình WiFi với các địa chỉ mạng được chỉ định.
Bạn có thể gọi WiFi.config () sau WiFi.begin (), sẽ khởi tạo ở chế độ DHCP mặc định. Khi phương thức config () được gọi, nó sẽ thay đổi địa chỉ mạng theo yêu cầu.
Cú pháp:
WiFi.config(ip); WiFi.config(ip, dns); WiFi.config(ip, dns, gateway); WiFi.config(ip, dns, gateway, subnet);
1.3 WIFI.config

## Slide 6: 1. WIFI CLASS
1.3 WIFI.config (example)
#include <SPI.h> #include <WiFi.h> IPAddress ip(192, 168, 0, 177); char ssid[] = "yourNetwork"; char pass[] = "secretPassword"; int status = WL_IDLE_STATUS; void setup() { Serial.begin(9600); while (!Serial) { ; } if (WiFi.status() == WL_NO_SHIELD) { Serial.println("WiFi shield not present"); while(true); // don't continue } WiFi.config(ip);
while ( status != WL_CONNECTED) { Serial.print("Attempting to connect to SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass); // wait 10 seconds for connection: delay(10000); } // print your WiFi shield's IP address: Serial.print("IP Address: "); Serial.println(WiFi.localIP()); } void loop () {}

## Slide 7: 1. WIFI CLASS
Cho phép định cấu hình máy chủ DNS (Domain Name System).
Cú pháp:
WiFi.setDNS(dns_server1)
WiFi.setDNS(dns_server1, dns_server2)
dns_server1: the IP address of the primary DNS server
dns_server2: the IP address of the secondary DNS server
1.4 WIFI.setDNS

## Slide 8: 1. WIFI CLASS
1.4 WIFI.setDNS (example)
#include <SPI.h> #include <WiFi.h> IPAddress dns(8, 8, 8, 8); char ssid[] = "yourNetwork"; char pass[] = "secretPassword"; int status = WL_IDLE_STATUS; void setup() { Serial.begin(9600); while (!Serial) { ; } if (WiFi.status() == WL_NO_SHIELD) { Serial.println("WiFi shield not present"); while(true); // don't continue }
while ( status != WL_CONNECTED) { Serial.print("Attempting to connect to SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass); delay(10000); } WiFi.setDNS(dns); Serial.print("Dns configured."); } void loop () { }

## Slide 9: 1. WIFI CLASS
Truy xuất SSID of mạng hiện tại
Cú pháp:
WiFi.SSID();
WiFi.SSID(wifiAccessPoint)
wifiAccessPoint: chỉ định mạng nào sẽ lấy thông tin
1.5 WIFI.SSID

## Slide 10: 1. WIFI CLASS
Quét các mạng WiFi khả dụng và trả về số được phát hiện
Cú pháp:
WiFi.scanNetworks();
1.6 WIFI.scanNetworks
#include <SPI.h> #include <WiFi.h> char ssid[] = "yourNetwork"; void setup() { Serial.begin(9600); int status = WiFi.begin(ssid); if (status != WL_CONNECTED) { Serial.println("Couldn't get a WiFi connection"); while (true); } else { Serial.println("** Scan Networks **"); byte numSsid = WiFi.scanNetworks(); Serial.print("Number of available WiFi networks discovered:"); Serial.println(numSsid); } } void loop() {}

## Slide 11: 1. WIFI CLASS
Trả về trạng thái kết nối
Cú pháp:
WiFi.status();
Giá trị return:
WL_CONNECTED: assigned when connected to a WiFi network;
WL_NO_SHIELD: assigned when no WiFi shield is present;
WL_IDLE_STATUS: it is a temporary status assigned when WiFi.begin() is called and remains active until the number of attempts expires (resulting in WL_CONNECT_FAILED) or a connection is established (resulting in WL_CONNECTED);
WL_NO_SSID_AVAIL: assigned when no SSID are available;
WL_SCAN_COMPLETED: assigned when the scan networks is completed;
WL_CONNECT_FAILED: assigned when the connection fails for all the attempts;
WL_CONNECTION_LOST: assigned when the connection is lost;
WL_DISCONNECTED: assigned when disconnected from a network;
1.7 WIFI.status

## Slide 12: 1. WIFI CLASS
1.7 WIFI.status (example)
#include <SPI.h> #include <WiFi.h> char ssid[] = "yourNetwork"; char key[] = "D0D0DEADF00DABBADEAFBEADED"; int keyIndex = 0; int status = WL_IDLE_STATUS; void setup() { Serial.begin(9600); while (!Serial) { ; } if (WiFi.status() == WL_NO_SHIELD) { Serial.println("WiFi shield not present"); // don't continue: while (true); }
while ( status != WL_CONNECTED) { Serial.print("Attempting to connect to WEP network, SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, keyIndex, key); // wait 10 seconds for connection: delay(10000); } // once you are connected : Serial.print("You're connected to the network"); } void loop() { // check the network status connection once every 10 seconds: delay(10000); Serial.println(WiFi.status()); }

## Slide 13: 1. WIFI CLASS
Nhận địa chỉ MAC của wifi hiện tại
Cú pháp:
WiFi.macAddress(mac);
Giá trị return:
byte array : 6 bytes representing the MAC address of your shield
1.8 WIFI.macAddress

## Slide 14: 1. WIFI CLASS
1.8 WIFI.macAddress (example)
#include <SPI.h> #include <WiFi.h> char ssid[] = "yourNetwork"; int status = WL_IDLE_STATUS; byte mac[6]; void setup() { Serial.begin(9600); status = WiFi.begin(ssid); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } // if you are connected, print your MAC address:
else { WiFi.macAddress(mac); Serial.print("MAC: "); Serial.print(mac[5],HEX); Serial.print(":"); Serial.print(mac[4],HEX); Serial.print(":"); Serial.print(mac[3],HEX); Serial.print(":"); Serial.print(mac[2],HEX); Serial.print(":"); Serial.print(mac[1],HEX); Serial.print(":"); Serial.println(mac[0],HEX); } } void loop () {}

## Slide 15: 2. IPAddress CLASS
Nhận địa chỉ IP của mạng cục bộ
Cú pháp:
WiFi. localIP();
2.1 WIFI.localIP
#include <WiFi.h> char ssid[] = "yourNetwork"; int status = WL_IDLE_STATUS; IPAddress ip; void setup() { Serial.begin(9600); WiFi.begin(ssid); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { //print the local IP address ip = WiFi.localIP(); Serial.println(ip); } } void loop () {}

## Slide 16: 2. IPAddress CLASS
Nhận địa chỉ subnet của mạng cục bộ
Cú pháp:
WiFi.subnetMask ();
2.2 WIFI.subnetMask
#include <WiFi.h> int status = WL_IDLE_STATUS; char ssid[] = "yourNetwork"; char pass[] = "secretPassword"; IPAddress ip; IPAddress subnet; IPAddress gateway; void setup() { WiFi.begin(ssid, pass); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { subnet = WiFi.subnetMask(); Serial.print("NETMASK: "); Serial.println(subnet); }} void loop () {
}

## Slide 17: 2. IPAddress CLASS
Nhận địa chỉ gateway của mạng cục bộ
Cú pháp:
WiFi.gatewayIP ();
2.3 WIFI.gatewayIP
#include <SPI.h> #include <WiFi.h> int status = WL_IDLE_STATUS; char ssid[] = "yourNetwork"; char pass[] = "secretPassword"; IPAddress gateway; void setup() { Serial.begin(9600); WiFi.begin(ssid, pass); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { gateway = WiFi.gatewayIP(); Serial.print("GATEWAY: "); Serial.println(gateway);} } void loop () {}

## Slide 18: 3. SEVER CLASS
Tạo một máy chủ lắng nghe các kết nối đến trên cổng được chỉ định.
Cú pháp:
Sever (port);
3.1 WIFIS ever
Serial.print("SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { server.begin(); Serial.print("Connected to wifi. My address:"); IPAddress myAddress = WiFi.localIP(); Serial.println(myAddress); } } void loop() { }
#include <SPI.h> #include <WiFi.h> char ssid[] = "myNetwork"; char pass[] = "myPassword"; int status = WL_IDLE_STATUS; WiFiServer server(80); void setup() { Serial.begin(9600); Serial.println("Attempting to connect to WPA network...");

## Slide 19: 3. SEVER CLASS
Có được một máy khách được kết nối với máy chủ và có sẵn dữ liệu để đọc. Kết nối vẫn tồn tại khi đối tượng máy khách được trả về nằm ngoài phạm vi; bạn có thể đóng nó bằng cách gọi client.stop ().
Cú pháp:
server.available();
3.2 sever.available

## Slide 20: 3. SEVER CLASS
3.3 sever.available (example)
#include <SPI.h> #include <WiFi.h> char ssid[] = "Network"; char pass[] = "myPassword"; int status = WL_IDLE_STATUS;
WiFiServer server(80);
void setup() { // initialize serial: Serial.begin(9600); Serial.println("Attempting to connect to WPA network..."); Serial.print("SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass);
if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { server.begin(); Serial.print("Connected to wifi. My address:"); IPAddress myAddress = WiFi.localIP(); Serial.println(myAddress); } } void loop() { WiFiClient client = server.available(); if (client) { if (client.connected()) { Serial.println("Connected to client"); } client.stop(); } }

## Slide 21: 3. SEVER CLASS
Ghi dữ liệu đến các clients đã kết nối với sever.
Cú pháp:
server.write(data);
data: byte hoặc char
Giá trị return:
byte: số byte đã được viết
3.4 sever.write
void setup() { Serial.begin(9600); Serial.println("Attempting to connect to WPA network..."); Serial.print("SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { server.begin(); } } void loop() { WiFiClient client = server.available(); if (client == true) { server.write(client.read()); }
#include <SPI.h> #include <WiFi.h> char ssid[] = "yourNetwork"; char pass[] = "yourPassword"; int status = WL_IDLE_STATUS; WiFiServer server(80);

## Slide 22: 3. SEVER CLASS
In dữ liệu đến các clients đã kết nối với sever.
Cú pháp:
server.print(data);
server.print(data, BASE);
data: byte, char, int, long hoặc string
base (optional): BIN (hệ 2), DEC (hệ 10), OCT (hệ 8), HEX (hệ 16).
3.5 sever.print – sever.println

## Slide 23: 4. Client CLASS
Tạo một máy khách có thể kết nối với một địa chỉ và cổng IP được chỉ định như được xác định trong client.connect ().
Cú pháp:
WiFiClient();
4.1 WiFiClient
Serial.println("Attempting to connect to WPA network..."); Serial.print("SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { Serial.println("Connected to wifi"); Serial.println("\nStarting connection..."); if (client.connect(server, 80)) { Serial.println("connected"); client.println("GET /search?q=arduino HTTP/1.0"); client.println(); } } } void loop() { }
#include <SPI.h> #include <WiFi.h> char ssid[] = "myNetwork"; char pass[] = "myPassword"; int status = WL_IDLE_STATUS; IPAddress server(74,125,115,105); WiFiClient client; void setup() { Serial.begin(9600);

## Slide 24: 4. Client CLASS
Kiểm tra xem client đã được kết nối chưa
Cú pháp:
client.connected();
4.2 Client.connected
if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); } else { Serial.println("Connected to wifi"); Serial.println("\nStarting connection..."); if (client.connect(server, 80)) { Serial.println("connected"); client.println("GET /search?q=arduino HTTP/1.0"); client.println(); } } } void loop() { if (client.available()) { char c = client.read(); Serial.print(c); } if (!client.connected()) { Serial.println(); Serial.println("disconnecting."); client.stop(); for(;;) ; } }
#include <SPI.h> #include <WiFi.h> char ssid[] = "myNetwork";
char pass[] = "myPassword"; int status = WL_IDLE_STATUS; IPAddress server(74,125,115,105); WiFiClient client; void setup() { Serial.begin(9600); Serial.println("Attempting to connect to WPA network..."); Serial.print("SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass);

## Slide 25: 4. Client CLASS
Kết nối với địa chỉ IP và cổng được chỉ định trong hàm tạo. Giá trị trả về cho biết thành công hay thất bại. Connect () cũng hỗ trợ tra cứu DNS khi sử dụng tên miền (ví dụ: google.com).
Cú pháp:
client.connect(ip, port);
client.connect(URL, port);
ip: the IP address that the client will connect to (array of 4 bytes)
URL: the domain name the client will connect to (string, ex.:"arduino.cc")
port: the port that the client will connect to (int)
4.3 client.connect

## Slide 26: 4. Client CLASS
4.3 client.connect (example)
#include <SPI.h> #include <WiFi.h> char ssid[] = "myNetwork"; char pass[] = "myPassword"; int status = WL_IDLE_STATUS; char servername[]="google.com"; WiFiClient client; void setup() { Serial.begin(9600); Serial.println("Attempting to connect to WPA network..."); Serial.print("SSID: "); Serial.println(ssid); status = WiFi.begin(ssid, pass); if ( status != WL_CONNECTED) { Serial.println("Couldn't get a wifi connection"); while(true); }
else { Serial.println("Connected to wifi"); Serial.println("\nStarting connection..."); if (client.connect(servername, 80)) { Serial.println("connected"); client.println("GET /search?q=arduino HTTP/1.0"); client.println(); } } } void loop() { }

## Slide 27: 4. Client CLASS
Ghi dữ liệu đến sever mà client đã kết nối
Cú pháp:
client.write(data)
data: the byte or char to write
4.4 client.write

## Slide 28: 4. Client CLASS
In dữ liệu đến sever mà client đã kết nối
Cú pháp:
client.print(data);
client.print(data, BASE);
client.println(); client.println(data); client.print(data, BASE);
data: byte, char, int, long hoặc string
base (optional): BIN (hệ 2), DEC (hệ 10), OCT (hệ 8), HEX (hệ 16).
4.5 client.print – client.println

## Slide 29: 4. Client CLASS
Đọc byte tiếp theo nhận được từ máy chủ mà máy khách được kết nối
Cú pháp:
client.read();
Giá trị return:
The next byte (or character)
4.6 client.read

## Slide 30: 4. Client CLASS
Hủy bỏ các byte nào đã được ghi cho máy khách nhưng chưa đọc.
Cú pháp:
client.flush();
4.7 client.flush

## Slide 31: 4. Client CLASS
Ngắt kết nối khỏi sever.
Cú pháp:
client.stop();
4.8 client.stop

## Slide 32
Diễn giả: Nguyễn Hoàng Phúc
Bộ phận: IoT Indruino