## Slide 2: WEBSEVER LOGIN WIFI SET MQTT
Diễn giả: Nguyễn Hoàng Phúc
Bộ phận: IoT Indruino

## Slide 3
PART 1:
Websever lib & log in wifi

## Slide 4: 1.1 GIAO DIỆN THAO TÁC
  Configure Wifi, Đăng nhập vào mạng
  Info, thông tin mạng và thông tin phần cứng
  Exit, ngắt kết nối

## Slide 5: 1.2 EXAMPLE BASIC
#include <WiFiManager.h> // https://github.com/tzapu/WiFiManager
void setup() {
WiFi.mode(WIFI_STA); // explicitly set mode, esp defaults to STA+AP
// put your setup code here, to run once:
Serial.begin(115200);
WiFiManager wm;
//reset settings - wipe credentials for testing
wm.resetSettings();
bool res;
// res = wm.autoConnect(); // auto generated AP name from chipid
// res = wm.autoConnect("AutoConnectAP");
// anonymous ap
res = wm.autoConnect("AutoConnectAP","password"); // password protected ap
if(!res) {
Serial.println("Failed to connect");
// ESP.restart();
}
else {
//if you get here you have connected to the WiFi
Serial.println("connected...yeey :)");
}
}
void loop() {
// put your main code here, to run repeatedly:
}

## Slide 6: 1.2 EXAMPLE BASIC
WiFi.mode: là lệnh set up các chế độ của wifi cụ thể là ESP32
WIFI_STA: là chế độ mặc định của esp vừa là trạm vừa là điểm truy cập access point
WiFi.mode(WIFI_STA); // explicitly set mode, esp defaults to STA+AP

## Slide 7: 1.2 EXAMPLE BASIC
WiFiManager wm;
Gọi tắt tên của WiFiManager với tên là wm
wm.resetSettings();
Trong khi test ta sử dụng reset để mở AP để setting sau mỗi lần khởi động
Tắt reset nếu đã hoàn thành công việc test sau khi set up wifi sẽ tắt AP để luôn luôn truy cập vào một điểm cố định đã được lưu vào bộ nhớ lưu trữ dữ liệu wifi

## Slide 8: 1.2 EXAMPLE BASIC
WiFiManager wm;
Gọi tắt tên của WiFiManager với tên là wm
wm.resetSettings();
Trong khi test ta sử dụng reset để mở AP để setting sau mỗi lần khởi động
Tắt reset nếu đã hoàn thành công việc test sau khi set up wifi sẽ tắt AP để luôn luôn truy cập vào một điểm cố định đã được lưu vào bộ nhớ lưu trữ dữ liệu wifi

## Slide 9: 1.2 EXAMPLE BASIC
res = wm.autoConnect();
res = wm.autoConnect("AutoConnectAP");
res = wm.autoConnect("AutoConnectAP","password");
Các lệnh trên có chức năng tương tự nhau do được set up với các kiểu template để người dụng tiện với thông tin có sẵn nào.
Lệnh trên được sử dụng để kết nối các mạng wifi đã có sẵn hoặc lưu trước đó

## Slide 10: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.1 resetSetting
void WiFiManager::resetSettings() {
DEBUG_WM(F("resetSettings"));
WiFi_enableSTA(true,true); // chuyển sang station
if (_resetcallback != NULL)
_resetcallback();
#ifdef ESP32
WiFi.disconnect(true,true); //ngắt kết nối trên station
#else
WiFi.persistent(true); // lưu lại trên rom của esp
WiFi.disconnect(true); // ngắt kết nối
WiFi.persistent(false); // chỉ thao tác nhưng không lưu lại
#endif
DEBUG_WM(F("SETTINGS ERASED"));
}

## Slide 11: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.2 Wifi_enableSTA – chuyển sang mode station
bool WiFiManager::WiFi_enableSTA(bool enable,bool persistent) {
DEBUG_WM(DEBUG_DEV,F("WiFi station enable"));
#ifdef ESP8266
WiFiMode_t newMode;
WiFiMode_t currentMode = WiFi.getMode();
bool isEnabled = (currentMode & WIFI_STA) != 0;
if(enable) newMode = (WiFiMode_t)(currentMode | WIFI_STA);
else newMode = (WiFiMode_t)(currentMode & (~WIFI_STA));
if((isEnabled != enable) || persistent) {
if(enable) {
if(persistent) DEBUG_WM(DEBUG_DEV,F("enableSTA PERSISTENT ON"));
return WiFi_Mode(newMode,persistent);}
else { return WiFi_Mode(newMode,persistent);
}
} else
{
return true; }
#elif defined(ESP32)
bool ret;
if(persistent && esp32persistent) WiFi.persistent(true);
ret = WiFi.enableSTA(enable); // @todo handle persistent when it is implemented in platform
if(persistent && esp32persistent) WiFi.persistent(false);
return ret;
#endif
}

## Slide 12: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.3 autoConnect()
boolean WiFiManager::autoConnect() {
String ssid = getDefaultAPName();
return autoConnect(ssid.c_str(), NULL);
}
/**
* [autoConnect description]
* @access public
* @param {[type]} char const *apName [description]
* @param {[type]} char const *apPassword [description]
* @return {[type]} [description]*/
boolean WiFiManager::autoConnect(char const *apName, char const *apPassword) {
DEBUG_WM(F("AutoConnect"));
if(getWiFiIsSaved()){
_begin();
if(!WiFi.enableSTA(true)){
// mở mode station
DEBUG_WM(DEBUG_ERROR,"[FATAL] Unable to enable wifi!");
return false;
}
WiFiSetCountry(); // cài đặt vùng của wifi
#ifdef ESP32
if(esp32persistent) WiFi.persistent(false);
// chỉ thao tác trên wifi nhưng không lưu
#endif
_usermode = WIFI_STA;
WiFi_autoReconnect();
// cài đặt hostname trước khi bắt đầu
if((String)_hostname != ""){
setupHostname(true);
}
bool connected = false;
if (WiFi.status() == WL_CONNECTED){
connected = true; // kiểm tra kết nối
DEBUG_WM(F("AutoConnect: ESP Already Connected"));
setSTAConfig();
// @todo not sure if this check makes sense, causes dup setSTAConfig in connectwifi,
// and we have no idea WHAT we are connected to
}
if(connected || connectWifi("", "") == WL_CONNECTED){
DEBUG_WM(F("AutoConnect: SUCCESS"));
DEBUG_WM(F("STA IP Address:"),WiFi.localIP());
_lastconxresult = WL_CONNECTED;
if((String)_hostname != ""){
#ifdef ESP8266
DEBUG_WM(DEBUG_DEV,"hostname: STA: ",WiFi.hostname());
#elif defined(ESP32)
DEBUG_WM(DEBUG_DEV,"hostname: STA: ",WiFi.getHostname());
#endif
}
return true; // connected success
}
// possibly skip the config portal
if (!_enableConfigPortal) {
return false; // not connected and not cp
}
DEBUG_WM(F("AutoConnect: FAILED"));
}
else DEBUG_WM(F("No Credentials are Saved, skipping connect"));
// not connected start configportal
bool res = startConfigPortal(apName, apPassword);
// set up mạng khi không kết nối
return res;
}

## Slide 13: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.4 getDefaultAPName()
String WiFiManager::getDefaultAPName(){
String hostString = String(WIFI_getChipId(),HEX);
// esp32//#define WIFI_getChipId() (uint32_t)ESP.getEfuseMac()
//8266 //#define WIFI_getChipId() ESP.getChipId()
hostString.toUpperCase();
// char hostString[16] = {0};
// sprintf(hostString, "%06X", ESP.getChipId());
return _wifissidprefix + "_" + hostString;
}

## Slide 14: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.5 getWiFiIsSaved()
bool WiFiManager::getWiFiIsSaved(){
return WiFi_hasAutoConnect();
}
bool WiFiManager::WiFi_hasAutoConnect(){
return WiFi_SSID(true) != "";
}
String WiFiManager::WiFi_SSID(bool persistent) const{
#ifdef ESP8266
struct station_config conf;
if(persistent) wifi_station_get_config_default(&conf);
else wifi_station_get_config(&conf);
char tmp[33]; //ssid can be up to 32chars, => plus null term
memcpy(tmp, conf.ssid, sizeof(conf.ssid));
tmp[32] = 0; //nullterm in case of 32 char ssid
return String(reinterpret_cast<char*>(tmp));
#elif defined(ESP32)
if(persistent){
wifi_config_t conf;
esp_wifi_get_config(WIFI_IF_STA, &conf);
return String(reinterpret_cast<const char*>(conf.sta.ssid));
}
else {
if(WiFiGenericClass::getMode() == WIFI_MODE_NULL){
return String();
}
wifi_ap_record_t info;
if(!esp_wifi_sta_get_ap_info(&info)) {
return String(reinterpret_cast<char*>(info.ssid));
}
return String();
}
#endif
}

## Slide 15: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.6 WiFi_autoReconnect()
void WiFiManager::WiFi_autoReconnect(){
#ifdef ESP8266
WiFi.setAutoReconnect(_wifiAutoReconnect);
#elif defined(ESP32)
// if(_wifiAutoReconnect){
// @todo move to seperate method, used for event listener now
DEBUG_WM(DEBUG_VERBOSE,"ESP32 event handler enabled");
using namespace std::placeholders;
wm_event_id = WiFi.onEvent(std::bind(&WiFiManager::WiFiEvent,this,_1,_2));
// }
#endif
}

## Slide 16: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.7 setupHostname()
bool WiFiManager::setupHostname(bool restart){
if((String)_hostname == "") {
DEBUG_WM(DEBUG_DEV,"No Hostname to set");
return false;
} else DEBUG_WM(DEBUG_DEV,"setupHostname: ",_hostname);
bool res = true;
#ifdef ESP8266
DEBUG_WM(DEBUG_VERBOSE,"Setting WiFi hostname");
res = WiFi.hostname(_hostname);
// #ifdef ESP8266MDNS_H
#ifdef WM_MDNS
DEBUG_WM(DEBUG_VERBOSE,"Setting MDNS hostname, tcp 80");
if(MDNS.begin(_hostname)){
MDNS.addService("http", "tcp", 80);
}
#endif
#elif defined(ESP32)
// @note hostname must be set after STA_START
delay(200); // do not remove, give time for STA_START
res = WiFi.setHostname(_hostname);
// #ifdef ESP32MDNS_H
#ifdef WM_MDNS
DEBUG_WM(DEBUG_VERBOSE,"Setting MDNS hostname, tcp 80");
if(MDNS.begin(_hostname)){
MDNS.addService("http", "tcp", 80);
}
#endif
#endif
if(!res)DEBUG_WM(DEBUG_ERROR,F("[ERROR] hostname: set failed!"));
// in sta mode restart , not sure about softap
if(restart && (WiFi.status() == WL_CONNECTED)){
DEBUG_WM(DEBUG_VERBOSE,F("reconnecting to set new hostname"));
// WiFi.reconnect(); // This does not reset dhcp
WiFi_Disconnect();
delay(200); // do not remove, need a delay for disconnect to change status()
}
return res;
}

## Slide 17: 1.3 WIFI MANAGER (EXAMPLE BASIC)
1.3.7 startConfigPortal()
boolean WiFiManager::startConfigPortal(char const *apName, char const *apPassword) {
_begin();
//setup AP
_apName = apName; // @todo check valid apname ?
_apPassword = apPassword;
DEBUG_WM(DEBUG_VERBOSE,F("Starting Config Portal"));
if(_apName == "") _apName = getDefaultAPName();
if(!validApPassword()) return false;
// HANDLE issues with STA connections, shutdown sta if not connected, or else this will hang channel scanning and softap will not respond
// @todo sometimes still cannot connect to AP for no known reason, no events in log either
if(_disableSTA || (!WiFi.isConnected() && _disableSTAConn)){
// this fixes most ap problems, however, simply doing mode(WIFI_AP) does not work if sta connection is hanging, must `wifi_station_disconnect`
WiFi_Disconnect();
WiFi_enableSTA(false);
DEBUG_WM(DEBUG_VERBOSE,F("Disabling STA")); }
else {
WiFi_enableSTA(true);
}
// init configportal globals to known states
configPortalActive = true;
bool result = connect = abort = false; // loop flags, connect true success, abort true break
uint8_t state;
_configPortalStart = millis();
// start access point
DEBUG_WM(DEBUG_VERBOSE,F("Enabling AP"));
startAP();
WiFiSetCountry();
// do AP callback if set
if ( _apcallback != NULL) {
_apcallback(this);
}

## Slide 18
PART 2:
Set & Print to terminal

## Slide 19: 2.1 PRINT TO TERMINAL
2.1.1 SET UP DEFAULT & FUNTION
typedef enum {
DEBUG_ERROR = 0,
DEBUG_NOTIFY = 1, // default stable
DEBUG_VERBOSE = 2,
DEBUG_DEV = 3, // default dev
DEBUG_MAX = 4
} wm_debuglevel_t;
boolean _debug = true;
// build debuglevel support
// @todo use DEBUG_ESP_x?
#ifdef M_DEBUG_LEVEL
uint8_t _debugLevel = (uint8_t)WM_DEBUG_LEVEL;
#else
uint8_t _debugLevel = DEBUG_DEV;
// default debug level
#endif
// @todo use DEBUG_ESP_PORT ?
#ifdef WM_DEBUG_PORT
Stream& _debugPort = WM_DEBUG_PORT;
#else
Stream& _debugPort = Serial; // debug output stream ref
#endif
template <typename Generic>
void DEBUG_WM(Generic text);
template <typename Generic>
void DEBUG_WM(wm_debuglevel_t level,Generic text);
template <typename Generic, typename Genericb>
void DEBUG_WM(Generic text,Genericb textb);
template <typename Generic, typename Genericb>
void DEBUG_WM(wm_debuglevel_t level, Generic text,Genericb textb);

## Slide 20: 2.1 PRINT TO TERMINAL
2.1.1 SET UP DEFAULT & FUNTION
typedef enum {
DEBUG_ERROR = 0,
DEBUG_NOTIFY = 1, // default stable
DEBUG_VERBOSE = 2,
DEBUG_DEV = 3, // default dev
DEBUG_MAX = 4
} wm_debuglevel_t;
boolean _debug = true;
// build debuglevel support
// @todo use DEBUG_ESP_x?
#ifdef M_DEBUG_LEVEL
uint8_t _debugLevel = (uint8_t)WM_DEBUG_LEVEL;
#else
uint8_t _debugLevel = DEBUG_DEV;
// default debug level
#endif
// @todo use DEBUG_ESP_PORT ?
#ifdef WM_DEBUG_PORT
Stream& _debugPort = WM_DEBUG_PORT;
#else
Stream& _debugPort = Serial; // debug output stream ref
#endif
template <typename Generic>
void DEBUG_WM(Generic text);
template <typename Generic>
void DEBUG_WM(wm_debuglevel_t level,Generic text);
template <typename Generic, typename Genericb>
void DEBUG_WM(Generic text,Genericb textb);
template <typename Generic, typename Genericb>
void DEBUG_WM(wm_debuglevel_t level, Generic text,Genericb textb);

## Slide 21: 2.1 PRINT TO TERMINAL
2.1.2 DEBUG_WM
template <typename Generic>
void WiFiManager::DEBUG_WM(Generic text) {
DEBUG_WM(DEBUG_NOTIFY,text,"");
} template <typename Generic>
void WiFiManager::DEBUG_WM(wm_debuglevel_t level,Generic text) {
if(_debugLevel >= level) DEBUG_WM(level,text,"");
} template <typename Generic, typename Genericb>
void WiFiManager::DEBUG_WM(Generic text,Genericb textb) {
DEBUG_WM(DEBUG_NOTIFY,text,textb);
} template <typename Generic, typename Genericb>
void WiFiManager::DEBUG_WM(wm_debuglevel_t level,Generic text,Genericb textb) {
if(!_debug || _debugLevel < level) return;
if(_debugLevel >= DEBUG_MAX){
uint32_t free;
uint16_t max;
uint8_t frag;
#ifdef ESP8266
ESP.getHeapStats(&free, &max, &frag);
_debugPort.printf("[MEM] free: %5d | max: %5d | frag: %3d%% \n", free, max, frag);
#elif defined ESP32
multi_heap_info_t info;
heap_caps_get_info(&info, MALLOC_CAP_INTERNAL);
free = info.total_free_bytes;
max = info.largest_free_block;
frag = 100 - (max * 100) / free;
_debugPort.printf("[MEM] free: %5d | max: %5d | frag: %3d%% \n", free, max, frag);
#endif
}
_debugPort.print("*WM: ");
if(_debugLevel == DEBUG_DEV) _debugPort.print("["+(String)level+"] ");
_debugPort.print(text);
if(textb){
_debugPort.print(" ");
_debugPort.print(textb);
}
_debugPort.println();
}

## Slide 22: 2.1 PRINT TO TERMINAL
2.1.3 GIAO DIỆN TERMINAL

## Slide 23: 2.1 PRINT TO TERMINAL
2.1.4 CODE PRINT TO TERMIAL (AP info)
void WiFiManager::debugSoftAPConfig(){
wifi_country_t country;
#ifdef ESP8266
softap_config config;
wifi_softap_get_config(&config);
wifi_get_country(&country);
#elif defined(ESP32)
wifi_config_t conf_config;
esp_wifi_get_config(WIFI_IF_AP, &conf_config);
wifi_ap_config_t config = conf_config.ap;
esp_wifi_get_country(&country);
#endif DEBUG_WM(F("SoftAP Configuration"));
DEBUG_WM(FPSTR(D_HR));
DEBUG_WM(F("ssid: "),(char *) config.ssid);
DEBUG_WM(F("password: "),(char *) config.password);
DEBUG_WM(F("ssid_len: "),config.ssid_len);
DEBUG_WM(F("channel: "),config.channel);
DEBUG_WM(F("authmode: "),config.authmode);
DEBUG_WM(F("ssid_hidden: "),config.ssid_hidden);
DEBUG_WM(F("max_connection: "),config.max_connection);
DEBUG_WM(F("country: "),(String)country.cc);
DEBUG_WM(F("beacon_interval: "),(String)config.beacon_interval + "(ms)");
DEBUG_WM(FPSTR(D_HR)); }

## Slide 24: 2.1 PRINT TO TERMINAL
2.1.5 CODE PRINT TO TERMIAL (AP Idaddress)
void WiFiManager::setupConfigPortal() {
DEBUG_WM(F("Starting Web Portal"));
// setup dns and web servers
dnsServer.reset(new DNSServer());
server.reset(new WM_WebServer(_httpPort));
if(_httpPort != 80) DEBUG_WM(DEBUG_VERBOSE,"http server started with custom port: ",_httpPort); // @todo not showing ip
/* Setup the DNS server redirecting all the domains to the apIP */
dnsServer->setErrorReplyCode(DNSReplyCode::NoError);
// DEBUG_WM("dns server started port: ",DNS_PORT);
DEBUG_WM(DEBUG_DEV,"dns server started with ip: ",WiFi.softAPIP()); // @todo not showing ip
dnsServer->start(DNS_PORT, F("*"), WiFi.softAPIP());
// @todo new callback, webserver started, callback cannot override handlers, but can grab them first
if ( _webservercallback != NULL) {
_webservercallback();
}

## Slide 25: 2.1 PRINT TO TERMINAL
2.1.6 CODE PRINT TO TERMIAL (WIFI CONNECT)
bool WiFiManager::wifiConnectNew(String ssid, String pass){
bool ret = false;
DEBUG_WM(F("CONNECTED:"),WiFi.status() == WL_CONNECTED);
DEBUG_WM(F("Connecting to NEW AP:"),ssid);
DEBUG_WM(DEBUG_DEV,F("Using Password:"),pass);
WiFi_enableSTA(true,storeSTAmode);
// storeSTAmode will also toggle STA on in default opmode (persistent) if true (default)
WiFi.persistent(true);
ret = WiFi.begin(ssid.c_str(), pass.c_str());
WiFi.persistent(false);
if(!ret) DEBUG_WM(DEBUG_ERROR,"[ERROR] wifi begin failed");
return ret;
}

## Slide 26: 2.1 PRINT TO TERMINAL
2.1.7 CODE PRINT TO TERMIAL (SHOW IP LOCAL)
if (connectWifi(_ssid, _pass) == WL_CONNECTED) {
DEBUG_WM(F("Connect to new AP [SUCCESS]"));
DEBUG_WM(F("Got IP Address:"));
DEBUG_WM(WiFi.localIP());
if ( _savewificallback != NULL) {
_savewificallback();
}
shutdownConfigPortal();
return WL_CONNECTED; // CONNECT SUCCESS
}

## Slide 27
Diễn giả: Nguyễn Hoàng Phúc
Bộ phận: IoT Indruino